## Slide 1: Automation Demo Topologies
https://github.com/JNPRAutomate/JNPRAutomateDemo-Class/

## Slide 2: Base Topology
Shared LAN: 10.10.0.0 /22
Head End Untrust:
10.10.0.5
Private Server:
192.168.10.10
vSRX Untrust:
ge-0/0/2: DHCP
vSRX Trust:
ge-0/0/1: 172.16.0.1
NetDevOps
eth1: 172.16.0.10
Student Vagrant Topology
Pod Details
Pod Number:
lo0 IP Address:
st0 IP Address:
IPSec VPN
int: st0.<pod_id>
zone: VPN
1

## Slide 3: Useful Commands and Links
vagrant up
  Start VM topology
vagrant suspend
  Put VMs into suspend mode, and maintain state
vagrant halt
  Power down and but do not delete all VMs in current directory
vagrant destroy
  Power down and delete all VMs in current directory
vagrant global-status
  Display a list of all Vagrant VMs currently running on the system
ansible-playbook
  -i <inventory file>
    Set which inventory file to use for the Ansbile run
  -u REMOTE_USER
    Connect as this user (default=vagrant)
  --ask-pass
    Prompt for user for SSH password to use for Ansible run
  --list-hosts
    outputs a list of matching hosts; does not execute anything else
  -v or –vvv
    Verbose mode (-vvv for more, -vvvv to enable connection debugging)
Vagrant Commands
Ansible Commands
@JNPRAutomation
github.com/JNPRAutomate